## Slide 1: 3D measurement based on computational photography fusing Passive stereo method and Depth from focus
Regional Planning and Information Lab
M2 Kajihara Yuki
Student Seminar (2018/10/26)

## Slide 2
Contents
1
Overview of my research
Background and Objective
Light field camera and its characteristic
Framework
Progress over three months
Plan from now on
Notes: 今後の展望はこのようになっています。

## Slide 3
Background and Objective
2
Increasing needs for low cost and accurate 3D measurement
Application areas：automatic driving, monitoring, entertainment
3D measurement using conventional camera
Device：Digital camera
Method：Passive stereo method (using images from different aspects)
Depth from focus (using images with different focus )
Passive stereo method
Depth from Focus
Camera 2
Camera 1
Img. 1
Img. 2
Eyes 1
Eyes 2
Img. 1
Img. 2
Img. 3
Img. 4
Img. 5

## Slide 4
Background and Objective
3
Disadvantage of using digital camera
Needs multiple shots or multiple cameras
Multiple shots：Takes much time / Invalid for moving objects
Multiple cameras：Calibration for each camera takes time / Errors
Disadvantage of passive stereo method
In case of repeating patterns on surface, matching ambiguity occurs
Disadvantage of Depth from focus
If brightness is too high, error occurs
Using a special camera which gives us many kinds of images by one shot and combining passive stereo method and Depth from focus, improve 3D measurement
Objective of this research

## Slide 5
Light field camera and its characteristic
4
Light field camera：Lytro Illum
History：A company named Lytro in the U.S started to sell in 2012
Place micro-lens-array between main lens and sensor
Light from object forms an image on micro-lens-array and is divided into rays on ray sensor
Lytro Illum
Structure of Lytro Illum
Micro-lens array
Ray sensor
Main lens

## Slide 6
Image from processing raw data
Multi-aspect image：Multiple images from slightly different aspects
Multi-focus image：Multiple images with slightly different focus
Light field camera and its characteristic
5
Multi-aspect image
Multi-focus image
Near Focus Far
http://www.cc.kyoto-su.ac.jp/~kano/pdf/study/student/2013HishinumaPaper.pdf

## Slide 7
Framework
6
.lfr image
.png image
Decode
Rearrange
Demosaic
.png images from different aspects
Rearrange
SIFT and feature matching
Parallax of each feature point
Stereo method
Matching cost ( Cs )
3D coordinates
.png images from different focuses
3D window Laplacian
depth of each point
Matching cost ( Cf )
Depth from focus
3D coordinates
Rearrange
3D coordinates
of feature points
Optimize
Square : data
Circle : Processing

## Slide 8
Framework
7
.lfr image
.png image
Decode
Rearrange
Demosaic
① Change the light field data into easy-to-handle form

## Slide 9
Framework
8
.lfr image
.png image
Decode
Rearrange
Demosaic
.png images from different aspects
Rearrange
SIFT and feature matching
Parallax of each feature point
Stereo method
Matching cost ( Cs )
3D coordinates
② 3D measurement using images from different aspects

## Slide 10
Framework
9
.lfr image
.png image
Decode
Rearrange
Demosaic
.png images from different aspects
Rearrange
SIFT and feature matching
Parallax of each feature point
Stereo method
Matching cost ( Cs )
3D coordinates
.png images from different focuses
3D window Laplacian
depth of each point
Matching cost ( Cf )
Depth from focus
3D coordinates
Rearrange
③ 3D measurement using images with different focuses

## Slide 11
Framework
10
.lfr image
.png image
Decode
Rearrange
Demosaic
.png images from different aspects
Rearrange
SIFT and feature matching
Parallax of each feature point
Stereo method
Matching cost ( Cs )
3D coordinates
.png images from different focuses
3D window Laplacian
depth of each point
Matching cost ( Cf )
Depth from focus
3D coordinates
Rearrange
3D coordinates
of feature points
Optimize
④ Extract 3D coordinates
by Minimizing cost

## Slide 12
Progress
11
Color : finished coding
Gray : not yet
.lfr image
.png image
Decode
Rearrange
Demosaic
.png images from different aspects
Rearrange
SIFT and feature matching
Parallax of each feature point
Stereo method
Matching cost ( Cs )
3D coordinates
.png images from different focuses
3D window Laplacian
depth of each point
Matching cost ( Cf )
Depth from focus
3D coordinates
Rearrange
3D coordinates
of feature points
Optimize
Now Coding

## Slide 13
①Change the light field data into easy-to-handle form
12
1. Decode .lfr file
Decoded image
.lfr image
.png image
Decode
Rearrange
Demosaic
.lfr file
・Gray image
・7728×5368 pixels
・Binary data
・need reverse engineering

## Slide 14
①Change the light field data into easy-to-handle form
13
2. Demosaic the image
Decoded image
Demosaiced image
.lfr image
.png image
Decode
Rearrange
Demosaic
・Lens placement is different
depending on even / odd row
・hard to handle when computing

## Slide 15
①Change the light field data into easy-to-handle form
14
3. Rearrange the image
Demosaiced image
Rearranged image
.lfr image
.png image
Decode
Rearrange
Demosaic
・Gray image
・5929×4752 pixels
・Gray image
・7728×5368 pixels
Based on coordinates
of centers of micro-lens
Notes: So, the next step is rearranging the image.

## Slide 16
1. Rearrange the image
②3D measurement using images from different aspects
15
.lfr image
.png image
Decode
Rearrange
Demosaic
.png images from different aspects
Rearrange
SIFT and feature matching
Parallax of each feature point
Stereo method
Matching cost ( Cs )
3D coordinates
Pick up and rearrange pixels according to
its relative coordinates from the center

## Slide 17
Slide show of obtained images ①Vertical
②3D measurement using images from different aspects
16

## Slide 25
Slide show of obtained images ②Horizontal
②3D measurement using images from different aspects
17

## Slide 33
2. SIFT and feature matching
②3D measurement using images from different aspects
18
.lfr image
.png image
Decode
Rearrange
Demosaic
.png images from different aspects
Rearrange
SIFT and feature matching
Parallax of each feature point
Stereo method
Matching cost ( Cs )
3D coordinates
As a trial, use images from
(-3, 0) aspect and (3, 0) aspect images

## Slide 34
2. SIFT and feature matching
②3D measurement using images from different aspects
19
Threshold: ①>②>③>④
①
②
③
④

## Slide 35
Plan from now on
20
Continue coding…
.lfr image
.png image
Decode
Rearrange
Demosaic
.png images from different aspects
Rearrange
SIFT and feature matching
Parallax of each feature point
Stereo method
Matching cost ( Cs )
3D coordinates
.png images from different focuses
3D window Laplacian
depth of each point
Matching cost ( Cf )
Depth from focus
3D coordinates
Rearrange
3D coordinates
of feature points
Optimize

## Slide 36
5

## Slide 37
Computational Photography
EX1
New field aiming to get all visual information of 3D scenes
：Computational Photography
History：Appeared in 1990s and drastically has developed in 3 decades
Characteristic：Redefine all process of imaging
Advantages：Adding to visual information from digital camera, we can
get depth and extend dynamic range by one shot
Field of Computational Photography
Sensor
Processing → Image
Lens
Object
Field of Conventional Photography

## Slide 38
2450 pixels
Light field camera and its characteristic
EX2
Basic information about Lytro Illum
Number of ray sensor：7728 × 5368
Number of pixels of output image：2450×1634
The content of raw data(.lfr) from Lytro：Color value of each sensor
Image from raw data of Lytro Illum
Raw image
1634 pixles

## Slide 39
Light field camera and its characteristic
EX3
Image from processing multi-focus image
Everywhere-focused image：Image with focus on every pixels
Multi-focus image
Everywhere-focused image

## Slide 40
Image Processing using Lytro Illum
EX4
Principle of getting raw image
Light ray from each point of an object is recorded on ray sensor
covered by micro-lens-array
For each micro-lens, average values of ray sensor and generate an
image focusing on the object → Raw image
Main lens
Micro-lens-array
Notes: 次に、画像の生成方法について説明します。物体の各点から発する光線は、マイクロレンズがカバーするいずれかの画素に記録されます。この図の場合は、ろうそく下部の赤い光が一番上のマイクロレンズアレイで結像し、その後方の3つの画素にそれぞれ記録されます。他の6つの点についても同様です。物体に焦点を合わせた画像の生成は、各マイクロレンズのカバーする画素の値を平均することで行われます。

## Slide 41
Image Processing using Lytro Illum
EX5
Principle of getting multi-aspect image
Can get multiple images from slightly different aspects by one shot
An image that sensors at the same position with respect to micro-lens
are arranged is a sub-aperture image seeing objects from a part of lens
When we say the number of ray sensor per micro-lens N, we can get
N multi-aspect image
Micro-lens-array
Aspect3
Lens
Aspect1
Aspect2
Notes: また、冒頭で述べたように、少しずつ視点の違った多視点画像を生成することもできます。各マイクロレンズに対して同じ位置の画素を再配列すると、レンズの一部から被写体を観察した画像が得られます。この図の場合は、それぞれのマイクロレンズの一番下の画素を追うことで、レンズ上部の赤い点線で囲われた領域からろうそくを見た図が生成されます。他の2つの視点についても同様です。このように、マイクロレンズ当たりの画素数に応じて、異なる視点の画像を得ることができます。

## Slide 42
Image Processing using Lytro Illum
EX6
Principle of getting multi-focus image
Can get multiple images with slightly different focus
Light rays which pass the pencil in the figure is recorded on ray
sensors covered by different micro-lens
By averaging, we can get an image with different focus from with
when we took the picture
Lens
Micro-lens-array
Notes: さらに、ライトフィールドカメラはピントの異なる画像を事後的に生成することもできます。例えば、この図はろうそくにピントを合わせた時の撮影状況を表していますが、前方に鉛筆があった場合、白丸を通過する光線は青い矢印で指された画素に記録されます。これらの画素値を平均することで、鉛筆にピントの合った画像を得ることができます。

## Slide 43
Study of method (Tentative)
EX7
Framework
Shot
and get raw data
Output Depth map
Get multi-aspect image
Get multi-focus image
Depth estimation by triangulation
Depth estimation by evaluation of focus
Integrate results
Choice
・Weighted average
・Peak ratio
・Markov random
field
Depth map

## Slide 44
Related works with passive stereo method and depth from focus①
EX8
Frese et al. (2006)
Device：Camera array of 3×3 digital cameras
Shot：Shoot 9 camera with different focus at the same time
Flamework：
Shot
Output Depth map
Get multi-aspect image
Get multi-focus image
Depth estimation by triangulation
Depth estimation by evaluation of focus
Verification of depth
Energy minimization problem
Step. 1
Step. 4
Step. 2
Step. 6
Step. 5
Step. 7
Energy minimization problem
Step. 3
Step. 1
Step. 1

## Slide 45
Step 3. Energy function about diaprity：E stereo (f)
E stereo (f) = E data (f) + E smoothness (f) + E visibility (f)
f ：Disparity when P in img. i has correspondence with Q in img. j
E data (f)：Square error of Intensity of P and Q
E smoothness (f)：
(Disparity between A and B when P has correspondence with A and B) minus
(Disparity between A and B when Q has correspondence with A and B)
E visibility (f)：Infinity when f is physically impossible
Related works with passive stereo method and depth from focus①
EX9
Img. 1
Img. 2
Img. i
Img. j
P
Q
A
A’
B
Disparity：α

## Slide 46
Related works with passive stereo method and depth from focus①
EX10
Step 6.
Verification of the value of Step.4 based on the value of Step.3
Based on the depth with passive stereo method from Step.2 and Step.3,
Verify the depth with depth from focus from Step.4 in terms of distance
between the base (In the following case, accuracy is P2>P3>P1)
Step 7.
Solve the new energy minimization problem： E fusion (f)
E fusion (f) = E stereo (f) + E focus (f)
E focus (f)：More accuracy, the smaller the value.
C2
C1
C3
Camera (look at C2)
π1
π2
π3
P1
P2
P3

## Slide 47
Related works with passive stereo method and depth from focus②
EX11
Tao et al. (2013)
Device：Lytro Illum
Flamework：
Shot
Combine by MRF
Get multi-aspect image
Get multi-focus image
Depth estimation by correspondence
Depth estimation by
focus analysis
Step. 1
Generate and shear EPI
Output depth map

## Slide 48
Plan from now on
EX12
Continue to review related works and methods
Re-consider about method
Improve the method of Frese et al. (2006) and Tao et al. (2013)
or completely different ways
Coding
Application of method
Capture scenes in environments where verification by actual distance
measurement is possible
Evaluate accuracy of method
Compare with passive stereo method, Depth from Focus,
the method of Frese et al. (2006) and Tao et al. (2013)
Notes: 今後の展望はこのようになっています。